## Slide 1: Computer System Overview
Dong Chen
Slide credits: © 2017 Pearson Education, Inc., Hoboken, NJ. All rights reserved.

## Slide 2: Operating System
Operating System (OS) is a collection of software that manages computer hardware resources
  Exploits the hardware resources of one or more processors
  Provides a set of services to system users
  Manages secondary memory and I/O devices
Notes: An operating system (OS) exploits the hardware resources of one or more processors to provide a set of services to system users. The OS also manages secondary memory and I/O (input/output) devices on behalf of its users. Accordingly, it is important to have some understanding of the underlying computer system hardware before we begin our examination of operating systems.
This chapter provides an overview of computer system hardware. In most areas, the survey is brief, as it is assumed that the reader is familiar with this subject. However,
several areas are covered in some detail because of their importance to topics
covered later in the book. Further topics are covered in Appendix C. For a more
detailed treatment, see [STAL16a].

## Slide 3: What’s An Operating System?
Operating System (OS)
  Definition has changed over years
  Interface between the user and the architecture
  Implements a “virtual machine” that is
  (Hopefully) easier to program than raw hardware
“even a ham sandwich”
(Microsoft to Dept of Justice)
Notes: https://github.com/CSCI-442-Mines/project-1-starter

## Slide 4
OS is a resource allocator
  Manages all resources
  Decides between conflicting requests for efficient and fair resource use
OS is a control program
  Controls execution of programs to prevent errors and improper use of the computer
What’s An Operating System?

## Slide 5: Overview
Cache memory
    Motivation
    Cache principles
    Cache design
Direct memory access
Multiprocessor and multicore organization
    Symmetric multiprocessors
    Multicore CPUs
Basic Elements
Evolution of the microprocessor
Instruction execution
Interrupts
    Interrupts and the instruction cycle
    Interrupt processing
    Multiple interrupts
The memory hierarchy
Notes: Summary of Chapter 1.

## Slide 6: Question Time?

## Slide 7: A typical PC computer system

## Slide 8: Example of Computer Systems

## Slide 9: Example of Computer Systems
Yahoo API
location
forecasting
Alerts
SQLite DB
push
push
push
RPC
RMI
Socket
Data cleaning

## Slide 10: Example of Computer Systems
Yahoo API
location
forecasting
Alerts
SQLite DB
push
push
push
RPC
RMI
Socket
Data cleaning
Android
iOS

## Slide 11: Example of Computer Systems
Yahoo API
location
forecasting
Alerts
SQLite DB
push
push
push
RPC
RMI
Socket
Data cleaning
Android
iOS
Cent OS, Ubuntu
ESX ? Xen?

## Slide 12: Example of Computer Systems
Yahoo API
location
forecasting
Alerts
SQLite DB
push
push
push
RPC
RMI
Socket
Data cleaning
Android
iOS
Cent OS, Ubuntu
ESX ? Xen?
Cent OS, Ubuntu,
Windows

## Slide 13: Example of Computer Systems
Yahoo API
location
forecasting
Alerts
SQLite DB
push
push
push
RPC
RMI
Socket
Data cleaning
Android
iOS
Cent OS, Ubuntu
ESX ? Xen?
Cent OS, Ubuntu,
Windows
Tiny OS, Wins CE

## Slide 14: Basic Elements of a Computer System
Processor
Main Memory
I/O Modules
System Bus
Notes: At a top level, a computer consists of processor, memory, and I/O components, with one or more modules of each type. These components are interconnected in some fashion to achieve the main function of the computer, which is to execute programs. Thus, there are four main structural elements:
Processor
I/O Modules
Main Memory
System Bus

## Slide 15: System Bus
  Provides for communication among processors, main memory, and I/O modules
exchange data with memory
Notes: System bus : Provides for communication among processors, main memory, and I/O modules.
Figure 1.1 depicts these top-level components. One of the processor’s functions is to exchange data with memory. For this purpose, it typically makes use of two internal (to the processor) registers: a memory address register (MAR), which specifies the address in memory for the next read or write; and a memory buffer register (MBR), which contains the data to be written into memory or which receives the data read from memory. Similarly, an I/O address register (I/OAR) specifies a particular I/O device. An I/O buffer register (I/OBR) is used for the exchange of data between an I/O module and the processor.
A memory module consists of a set of locations, defined by sequentially numbered addresses. Each location contains a bit pattern that can be interpreted as either an instruction or data. An I/O module transfers data from external devices to processor and memory, and vice versa. It contains internal buffers for temporarily holding data until they can be sent on.

## Slide 16: System Bus
  Provides for communication among processors, main memory, and I/O modules
exchange data with memory
Why do we need a I/O Buffer?
Notes: System bus : Provides for communication among processors, main memory, and I/O modules.
Figure 1.1 depicts these top-level components. One of the processor’s functions is to exchange data with memory. For this purpose, it typically makes use of two internal (to the processor) registers: a memory address register (MAR), which specifies the address in memory for the next read or write; and a memory buffer register (MBR), which contains the data to be written into memory or which receives the data read from memory. Similarly, an I/O address register (I/OAR) specifies a particular I/O device. An I/O buffer register (I/OBR) is used for the exchange of data between an I/O module and the processor.
A memory module consists of a set of locations, defined by sequentially numbered addresses. Each location contains a bit pattern that can be interpreted as either an instruction or data. An I/O module transfers data from external devices to processor and memory, and vice versa. It contains internal buffers for temporarily holding data until they can be sent on.

## Slide 17: Processor
Controls the operation of the computer
Performs the data processing functions
Referred to as the Central Processing Unit (CPU)
When there is only one processor, it is often referred to as the central processing unit (CPU).
Notes: Processor : Controls the operation of the computer and performs its data processing functions. When there is only one processor, it is often referred to as the central processing unit (CPU).

## Slide 18: Main Memory
Stores data and programs
Typically, volatile
  Contents of the memory is lost when the computer is shut down
Referred to as real memory or primary memory
Notes: Main memory : Stores data and programs. This memory is typically volatile; that is, when the computer is shut down, the contents of the memory are lost. In contrast, the contents of disk memory are retained even when the computer system is shut down. Main memory is also referred to as real memory or primary memory.

## Slide 19: Types of Memory
Memory: any device which can store information temporarily or permanently.
  Registers: temporary memory which the CPU can use for instruction operands.
  Cache: (fast) memory close to the CPU that mirrors values from RAM.
  RAM (Random Access Memory): temporary memory, often off the CPU, which allows access at any point without seeking.
  ROM (Read Only Memory): permanent memory, often used to contain the instructions to boot a machine. Sometimes reprogrammable (using tools like flash Rom).
  Also: consider hard drives, flash drives, CD-ROMs, floppies, tape drives, ...
Notes: Random Access = Directly Access

## Slide 20: Storage-device hierarchy

## Slide 21: I/O Modules
Move data between the computer and its external environment
Secondary memory devices (e.g. disks)
Communications equipment
(e.g. cameras)
Terminals
Notes: I/O modules : Move data between the computer and its external environment. The external environment consists of a variety of devices, including secondary
memory devices (e.g., disks), communications equipment, and terminals.

## Slide 22: A Modern System Architecture
I/O Modules

## Slide 23: Microprocessor
  Invention that brought desktop and handheld computing
  Contains a processor on a single chip
  Fastest general purpose processors
  Multiprocessors on a socket
  Each chip (socket) contains multiple processors (cores)
  Mostly common form: Central Processing Unit (CPU)
Notes: The hardware revolution that brought about desktop and handheld computing was the invention of the microprocessor, which contained a processor on a single chip. Though originally much slower than multichip processors, microprocessors have continually evolved to the point that they are now much faster for most computations due to the physics involved in moving information around in sub-nanosecond timeframes.
Not only have microprocessors become the fastest general purpose processors available, they are now multiprocessors; each chip (called a socket) contains multiple processors (called cores), each with multiple levels of large memory caches, and multiple logical processors sharing the execution units of each core. As of 2010, it is not unusual for even a laptop to have 2 or 4 cores, each with 2 hardware threads, for a total of 4 or 8 logical processors.

## Slide 24: Graphical Processing Units (GPUs)
  Provide efficient computation on arrays of data using Single-Instruction Multiple Data (SIMD) techniques pioneered in supercomputers
  Used in:
    Graphics
    Machine Learning
    Numerical Processing
Notes: Although processors provide very good performance for most forms of computing, there is increasing demand for numerical computation. Graphical Processing Units (GPUs) provide efficient computation on arrays of data using Single-Instruction Multiple Data (SIMD) techniques pioneered in supercomputers. GPUs are no longer used just for rendering advanced graphics, but they are also used for general numerical processing, such as physics simulations for games or computations on large spreadsheets. Simultaneously, the CPUs themselves are gaining the capability of operating on arrays of data—with increasingly powerful vector units integrated into the processor architecture of the x86 and AMD64 families.
Processors and GPUs are not the end of the computational story for the modern PC.
Numerical: new meri cal

## Slide 25: Digital Signal Processors (DSPs)
  Deal with streaming signals such as audio or video
  Encoding/decoding speech and video (codecs)
  Provide support for encryption and security
  Used to be embedded in I/O devices like modems
      Are now becoming first-class computational devices, especially in handhelds
      Evolved into Domain Specific Processors (DSP)
Notes: Digital Signal Processors (DSPs) are also present, for dealing with streaming signals—such as audio or video. DSPs used to be embedded in I/O devices, like modems, but they are now becoming first-class computational devices, especially in handhelds. Other specialized computational devices (fixed function units) co-exist with the CPU to support other standard computations, such as encoding/decoding speech and video (codecs), or providing support for encryption and security.

## Slide 26: System on a Chip (SoC)
To satisfy the requirements of handheld devices, the classic microprocessor is giving way to the SoC
    Other components of the system, such as DSPs, GPUs, I/O devices (such as codecs and radios) and main memory, in addition to the CPUs and caches, are on the same chip.
Notes: To satisfy the requirements of handheld devices, the classic microprocessor is giving way to the System on a Chip (SoC), where not just the CPUs and caches are on the same chip, but also many of the other components of the system, such as DSPs, GPUs, I/O devices (such as radios and codecs), and main memory.

## Slide 27: Instruction Execution
A program consists of a set of instructions stored in memory
Processor reads (fetches) instructions from memory
Processor executes each instruction
Two steps
Notes: A program to be executed by a processor consists of a set of instructions stored in memory. In its simplest form, instruction processing consists of two steps: The processor reads ( fetches ) instructions from memory one at a time and executes each instruction. Program execution consists of repeating the process of instruction fetch and instruction execution. Instruction execution may involve several operations and depends on the nature of the instruction.

## Slide 28: Instruction Execution
Notes: The processing required for a single instruction is called an instruction cycle. Using a simplified two-step description, the instruction cycle is depicted in Figure 1.2 . The two steps are referred to as the fetch stage and the execute stage. Program execution halts only if the processor is turned off, some sort of unrecoverable error occurs, or a program instruction that halts the processor is encountered.

## Slide 29: Instruction Fetch and Execute
The processor fetches an instruction from memory
Typically, the program counter (PC) holds the address of the next instruction to be fetched
      PC is incremented after each fetch
Notes: At the beginning of each instruction cycle, the processor fetches an instruction from memory. Typically, the program counter (PC) holds the address of the next instruction to be fetched. Unless instructed otherwise, the processor always increments the PC after each instruction fetch so that it will fetch the next instruction in sequence (i.e., the instruction located at the next higher memory address).
For example, consider a simplified computer in which each instruction occupies one
16-bit word of memory. Assume that the program counter is set to location 300.
The processor will next fetch the instruction at location 300. On succeeding instruction
cycles, it will fetch instructions from locations 301, 302, 303, and so on. This
sequence may be altered, as explained subsequently.

## Slide 30: Instruction Register (IR)
Fetched instruction is loaded into Instruction Register (IR)
Fetched instruction is loaded into Instruction Register (IR)
Processor interprets the instruction and performs required action:
      Processor-memory
      Processor-I/O
      Data processing
      Control
Notes: The fetched instruction is loaded into the instruction register (IR). The instruction contains bits that specify the action the processor is to take. The processor interprets the instruction and performs the required action. In general, these actions fall into four categories:
• Processor-memory: Data may be transferred from processor to memory or from memory to processor.
• Processor-I/O: Data may be transferred to or from a peripheral device by transferring between the processor and an I/O module.
• Data processing: The processor may perform some arithmetic or logic operation on data.
• Control: An instruction may specify that the sequence of execution be altered. For example, the processor may fetch an instruction from location 149, which
specifies that the next instruction be from location 182. The processor sets the
program counter to 182. Thus, on the next fetch stage, the instruction will be
fetched from location 182 rather than 150.
An instruction’s execution may involve a combination of these actions.

## Slide 31
Notes: Consider a simple example using a hypothetical processor that includes the characteristics listed in Figure 1.3 . The processor contains a single data register, called the accumulator (AC). Both instructions and data are 16 bits long, and memory is organized as a sequence of 16-bit words. The instruction format provides 4 bits for the opcode, allowing as many as 24 =16 different opcodes (represented by a single hexadecimal digit). The opcode defines the operation the processor is to perform. With the remaining 12 bits of the instruction format, up to 212 =4,096 (4K) words of memory (denoted by three hexadecimal digits) can be directly addressed.

## Slide 32: Hexadecimal
Assume your answer is 10, please do not answer 10 in your exam, your answer should be A

## Slide 33
  Instruction 1: Load AC from memory address 940
  Instruction 2: Increment the value of AC by the content of memory location 941.
  Instruction 3:. Store AC to memory location 941.
Notes: Figure 1.4 illustrates a partial program execution, showing the relevant portions of memory and processor registers. The program fragment shown adds the contents of the memory word at address 940 to the contents of the memory word at address 941 and stores the result in the latter location. Three instructions, which can be described as three fetch and three execute stages, are required:
The PC contains 300, the address of the first instruction. This instruction (the value 1940 in hexadecimal) is loaded into the IR and the PC is incremented. Note that this process involves the use of a memory address register (MAR) and a memory buffer register (MBR). For simplicity, these intermediate registers are not shown.
2. The first 4 bits (first hexadecimal digit) in the IR indicate that the AC is to be loaded from memory. The remaining 12 bits (three hexadecimal digits) specify the address, which is 940.
3. The next instruction (5941) is fetched from location 301 and the PC is incremented.
4. The old contents of the AC and the contents of location 941 are added and the result is stored in the AC.
5. The next instruction (2941) is fetched from location 302 and the PC is incremented.
6. The contents of the AC are stored in location 941.
In this example, three instruction cycles, each consisting of a fetch stage and
an execute stage, are needed to add the contents of location 940 to the contents
of 941. With a more complex set of instructions, fewer instruction cycles would be
needed. Most modern processors include instructions that contain more than one
address. Thus the execution stage for a particular instruction may involve more than
one reference to memory. Also, instead of memory references, an instruction may
specify an I/O operation.

## Slide 34: Instruction 1
Instruction 1: Load AC from memory address 940

## Slide 35: Instruction 1
Instruction 1: Load AC from memory address 940
Binary: 0001 1001 0100 0000

## Slide 36: Instruction 1
Instruction 1: Load AC from memory address 940
Binary: 0001 1001 0100 0000
Thus, Convert Binary to Hex: 1 9 4 0

## Slide 37: Instruction 2
Instruction 1: Increment the value of AC by the content of memory location 941
Binary: 0101 1001 0100 0001
Thus, Convert Binary to Hex: 5 9 4 1
Fetch
Execute

## Slide 38: Instruction 3
Instruction 1: Store AC to memory location 941.
Binary: 0010 1001 0100 0001
Thus, Convert Binary to Hex: 2 9 4 1
Fetch
Execute

## Slide 39
  Instruction 1: Load AC from memory address 940
  Instruction 2: Increment the value of AC by the content of memory location 941.
  Instruction 3:. Store AC to memory location 941.
Notes: Figure 1.4 illustrates a partial program execution, showing the relevant portions of memory and processor registers. The program fragment shown adds the contents of the memory word at address 940 to the contents of the memory word at address 941 and stores the result in the latter location. Three instructions, which can be described as three fetch and three execute stages, are required:
The PC contains 300, the address of the first instruction. This instruction (the value 1940 in hexadecimal) is loaded into the IR and the PC is incremented. Note that this process involves the use of a memory address register (MAR) and a memory buffer register (MBR). For simplicity, these intermediate registers are not shown.
2. The first 4 bits (first hexadecimal digit) in the IR indicate that the AC is to be loaded from memory. The remaining 12 bits (three hexadecimal digits) specify the address, which is 940.
3. The next instruction (5941) is fetched from location 301 and the PC is incremented.
4. The old contents of the AC and the contents of location 941 are added and the result is stored in the AC.
5. The next instruction (2941) is fetched from location 302 and the PC is incremented.
6. The contents of the AC are stored in location 941.
In this example, three instruction cycles, each consisting of a fetch stage and
an execute stage, are needed to add the contents of location 940 to the contents
of 941. With a more complex set of instructions, fewer instruction cycles would be
needed. Most modern processors include instructions that contain more than one
address. Thus the execution stage for a particular instruction may involve more than
one reference to memory. Also, instead of memory references, an instruction may
specify an I/O operation.

## Slide 40
HW#1.Q1: Suppose the hypothetical processor of Figure 1.3 also has two I/O instructions:
  0011 = Load AC from I/O 0111 = Store AC to I/O 0101 = Add to AC from memory
In these cases, the 12-bit address identifies a particular external device. Show the state of the memory content and CPU registers on the figure below for the following program:
  1. Load AC from device 3.
  2. Increment the value of AC by the content of memory location 946.
  3. Store AC to device 1.
Assume that the next value retrieved from device 3 is 10 and that location 946 contains a value of 4
Problem Time

## Slide 41: Interrupts
Mechanism by which other modules may interrupt the normal sequencing of the processor virtually.
Provided to improve processor utilization
    Most I/O devices are slower than the processor
    Processor must pause to wait for device
    Wasteful use of the processor
Notes: Virtually all computers provide a mechanism by which other modules (I/O, memory) may interrupt the normal sequencing of the processor.
Interrupts are provided primarily as a way to improve processor utilization. For example, most I/O devices are much slower than the processor. Suppose that the processor is transferring data to a printer using the instruction cycle scheme of Figure 1.2 . After each write operation, the processor must pause and remain idle until the printer catches up. The length of this pause may be on the order of many thousands or even millions of instruction cycles. Clearly, this is a very wasteful use of the processor.

## Slide 42
Four Different Classes/Reasons of Interrupts
Program Generated by some condition that occurs as a result of an instruction execution, such as arithmetic overflow, division by zero, attempt to execute an illegal machine instruction, and reference outside a user's allowed memory space.
Timer Generated by a timer within the processor. This allows the operating system to perform certain functions on a regular basis.
I/O Generated by an I/O controller, to signal normal completion of an operation or to signal a variety of error conditions.
Hardware Generated by a failure, such as power failure or memory
failure parity error.
Notes: Table 1.1 lists the most common classes of interrupts.

## Slide 43: Figure 1.5 Program flow of control with and without interrupts
I/O Command Interleaved with program execution
Long I/O Command Interleaved with program execution
Code: 1-> 4 -> 5 ->2 -> 3.
Code segments 1, 2, and 3 refer to sequences of instructions that do not involve I/O.
We can not run 2, 3 until 5 is done.
Notes: To give a specific example, consider a PC that operates at 1 GHz, which would allow roughly 109 instructions per second. A typical hard disk has a rotational speed of 7200 revolutions per minute for a half-track rotation time of 4 ms, which is 4 million times slower than the processor.
Figure 1.5a illustrates this state of affairs. The user program performs a series of WRITE calls interleaved with processing. The solid vertical lines represent segments of code in a program. Code segments 1, 2, and 3 refer to sequences of instructions that do not involve I/O. The WRITE calls are to an I/O routine that is a system utility and that will perform the actual I/O operation. The I/O program consists of three sections:
• A sequence of instructions, labeled 4 in the figure, to prepare for the actual I/O operation. This may include copying the data to be output into a special buffer and preparing the parameters for a device command.
• The actual I/O command. Without the use of interrupts, once this command is issued, the program must wait for the I/O device to perform the requested function (or periodically check the status, or poll, the I/O device). The program might wait by simply repeatedly performing a test operation to determine if the I/O operation is done.
• A sequence of instructions, labeled 5 in the figure, to complete the operation. This may include setting a flag indicating the success or failure of the operation.
The dashed line represents the path of execution followed by the processor; that is, this line shows the sequence in which instructions are executed. Thus, after the first WRITE instruction is encountered, the user program is interrupted and execution continues with the I/O program. After the I/O program execution is complete, execution resumes in the user program immediately following the WRITE Instruction.
Because the I/O operation may take a relatively long time to complete, the I/O program is hung up waiting for the operation to complete; hence, the user program is stopped at the point of the WRITE call for some considerable period of time. With interrupts, the processor can be engaged in executing other instructions while an I/O operation is in progress. Consider the flow of control in Figure 1.5b . As before, the user program reaches a point at which it makes a system call in the form of a WRITE call. The I/O program that is invoked in this case consists only of the preparation code and the actual I/O command. After these few instructions have been executed, control returns to the user program. Meanwhile, the external device is busy accepting data from computer memory and printing it. This I/O operation is conducted concurrently with the execution of instructions in the user program.
When the external device becomes ready to be serviced, that is, when it is ready to accept more data from the processor, the I/O module for that external device sends an interrupt request signal to the processor. The processor responds by suspending operation of the current program; branching off to a routine to service that particular I/O device, known as an interrupt handler; and resuming the original execution after the device is serviced. The points at which such interrupts occur are indicated by X in Figure 1.5b . Note that an interrupt can occur at any point in the main program, not just at one specific instruction.

## Slide 44: Figure 1.5 Program flow of control with and without interrupts
Can take very long !
Execution is blocked !!
I/O Command Interleaved with program execution
Long I/O Command Interleaved with program execution
Code: 1-> 4 -> 5 ->2 -> 3.
Code segments 1, 2, and 3 refer to sequences of instructions that do not involve I/O.
We can not run 2, 3 until 5 is done. (What is CPU doing now?)
Notes: To give a specific example, consider a PC that operates at 1 GHz, which would allow roughly 109 instructions per second. A typical hard disk has a rotational speed of 7200 revolutions per minute for a half-track rotation time of 4 ms, which is 4 million times slower than the processor.
Figure 1.5a illustrates this state of affairs. The user program performs a series of WRITE calls interleaved with processing. The solid vertical lines represent segments of code in a program. Code segments 1, 2, and 3 refer to sequences of instructions that do not involve I/O. The WRITE calls are to an I/O routine that is a system utility and that will perform the actual I/O operation. The I/O program consists of three sections:
• A sequence of instructions, labeled 4 in the figure, to prepare for the actual I/O operation. This may include copying the data to be output into a special buffer and preparing the parameters for a device command.
• The actual I/O command. Without the use of interrupts, once this command is issued, the program must wait for the I/O device to perform the requested function (or periodically check the status, or poll, the I/O device). The program might wait by simply repeatedly performing a test operation to determine if the I/O operation is done.
• A sequence of instructions, labeled 5 in the figure, to complete the operation. This may include setting a flag indicating the success or failure of the operation.
The dashed line represents the path of execution followed by the processor; that is, this line shows the sequence in which instructions are executed. Thus, after the first WRITE instruction is encountered, the user program is interrupted and execution continues with the I/O program. After the I/O program execution is complete, execution resumes in the user program immediately following the WRITE Instruction.
Because the I/O operation may take a relatively long time to complete, the I/O program is hung up waiting for the operation to complete; hence, the user program is stopped at the point of the WRITE call for some considerable period of time. With interrupts, the processor can be engaged in executing other instructions while an I/O operation is in progress. Consider the flow of control in Figure 1.5b . As before, the user program reaches a point at which it makes a system call in the form of a WRITE call. The I/O program that is invoked in this case consists only of the preparation code and the actual I/O command. After these few instructions have been executed, control returns to the user program. Meanwhile, the external device is busy accepting data from computer memory and printing it. This I/O operation is conducted concurrently with the execution of instructions in the user program.
When the external device becomes ready to be serviced, that is, when it is ready to accept more data from the processor, the I/O module for that external device sends an interrupt request signal to the processor. The processor responds by suspending operation of the current program; branching off to a routine to service that particular I/O device, known as an interrupt handler; and resuming the original execution after the device is serviced. The points at which such interrupts occur are indicated by X in Figure 1.5b . Note that an interrupt can occur at any point in the main program, not just at one specific instruction.

## Slide 45: Figure 1.5 Program flow of control with and without interrupts
Can take very long !
Execution is blocked !!
I/O Command Interleaved with program execution
Long I/O Command Interleaved with program execution
Notes: To give a specific example, consider a PC that operates at 1 GHz, which would allow roughly 109 instructions per second. A typical hard disk has a rotational speed of 7200 revolutions per minute for a half-track rotation time of 4 ms, which is 4 million times slower than the processor.
Figure 1.5a illustrates this state of affairs. The user program performs a series of WRITE calls interleaved with processing. The solid vertical lines represent segments of code in a program. Code segments 1, 2, and 3 refer to sequences of instructions that do not involve I/O. The WRITE calls are to an I/O routine that is a system utility and that will perform the actual I/O operation. The I/O program consists of three sections:
• A sequence of instructions, labeled 4 in the figure, to prepare for the actual I/O operation. This may include copying the data to be output into a special buffer and preparing the parameters for a device command.
• The actual I/O command. Without the use of interrupts, once this command is issued, the program must wait for the I/O device to perform the requested function (or periodically check the status, or poll, the I/O device). The program might wait by simply repeatedly performing a test operation to determine if the I/O operation is done.
• A sequence of instructions, labeled 5 in the figure, to complete the operation. This may include setting a flag indicating the success or failure of the operation.
The dashed line represents the path of execution followed by the processor; that is, this line shows the sequence in which instructions are executed. Thus, after the first WRITE instruction is encountered, the user program is interrupted and execution continues with the I/O program. After the I/O program execution is complete, execution resumes in the user program immediately following the WRITE Instruction.
Because the I/O operation may take a relatively long time to complete, the I/O program is hung up waiting for the operation to complete; hence, the user program is stopped at the point of the WRITE call for some considerable period of time. With interrupts, the processor can be engaged in executing other instructions while an I/O operation is in progress. Consider the flow of control in Figure 1.5b . As before, the user program reaches a point at which it makes a system call in the form of a WRITE call. The I/O program that is invoked in this case consists only of the preparation code and the actual I/O command. After these few instructions have been executed, control returns to the user program. Meanwhile, the external device is busy accepting data from computer memory and printing it. This I/O operation is conducted concurrently with the execution of instructions in the user program.
When the external device becomes ready to be serviced, that is, when it is ready to accept more data from the processor, the I/O module for that external device sends an interrupt request signal to the processor. The processor responds by suspending operation of the current program; branching off to a routine to service that particular I/O device, known as an interrupt handler; and resuming the original execution after the device is serviced. The points at which such interrupts occur are indicated by X in Figure 1.5b . Note that an interrupt can occur at any point in the main program, not just at one specific instruction.

## Slide 46: Figure 1.5 Program flow of control with interrupts

## Slide 47: Figure 1.5 Program flow of control with interrupts

## Slide 48: Figure 1.5 Program flow of control with interrupts

## Slide 49: Figure 1.5 Program flow of control with interrupts

## Slide 50: Figure 1.5 Program flow of control with interrupts

## Slide 51: Figure 1.5 Program flow of control with interrupts

## Slide 52: Figure 1.5 Program flow of control with interrupts

## Slide 53: Figure 1.5 Program flow of control with interrupts

## Slide 54: Figure 1.5 Program flow of control with interrupts

## Slide 55: Figure 1.5 Program flow of control with interrupts

## Slide 56: Figure 1.5 Program flow of control with interrupts

## Slide 57: Figure 1.5 Program flow of control with interrupts

## Slide 58: Figure 1.5 Program flow of control with interrupts

## Slide 59: Figure 1.5 Program flow of control with interrupts

## Slide 60: Figure 1.5 Program flow of control with interrupts

## Slide 61: Figure 1.5 Program flow of control with interrupts

## Slide 62
Who needs to accommodate interrupts?
For the user program, an interrupt suspends the normal sequence of execution.
Notes: For the user program, an interrupt suspends the normal sequence of execution. When the interrupt processing is completed, execution resumes ( Figure 1.6 ). Thus, the user program does not have to contain any special code to accommodate interrupts; the processor and the OS are responsible for suspending the user program and then resuming it at the same point.

## Slide 63
Notes: To appreciate the gain in efficiency, consider Figure 1.8 , which is a timing diagram based on the flow of control in Figures 1.5a and 1.5b . Figures 1.5b and 1.8 assume that the time required for the I/O operation is relatively short: less than the time to complete the execution of instructions between write operations in the user program. The more typical case, especially for a slow device such as a printer, is that the I/O operation will take much more time than executing a sequence of user instructions. Figure 1.5c indicates this state of affairs. In this case, the user program reaches the second WRITE call before the I/O operation spawned by the first call is complete. The result is that the user program is hung up at that point. When the preceding I/O operation is completed, this new WRITE call may be processed, and a new I/O operation may be started. Figure 1.9 shows the timing for this situation with and without the use of interrupts. We can see that there is still a gain in efficiency because part of the time during which the I/O operation is underway overlaps with the execution of user instructions.

## Slide 64
Notes: To accommodate interrupts, an interrupt stage is added to the instruction cycle, as shown in Figure 1.7 (compare Figure 1.2 ). In the interrupt stage, the processor checks to see if any interrupts have occurred, indicated by the presence of an interrupt signal. If no interrupts are pending, the processor proceeds to the fetch stage and fetches the next instruction of the current program. If an interrupt is pending, the processor suspends execution of the current program and executes an interrupt handler routine. The interrupt-handler routine is generally part of the OS. Typically, this routine determines the nature of the interrupt and performs whatever actions are needed. In the example we have been using, the handler determines which I/O module generated the interrupt and may branch to a program that will write more data out to that I/O module. When the interrupt-handler routine is completed, the processor can resume execution of the user program at the point of interruption.
It is clear that there is some overhead involved in this process. Extra instructions must be executed (in the interrupt handler) to determine the nature of the interrupt and to decide on the appropriate action. Nevertheless, because of the relatively large amount of time that would be wasted by simply waiting on an I/O operation, the processor can be employed much more efficiently with the use of interrupts.

## Slide 65: Question Time
True or False Question.
A typical CPU on a general-purpose computer checks for interrupts after execution of every instruction.
  A. TRUE
  B. FALSE

## Slide 66: Question Time
True or False Question.
A typical CPU on a general-purpose computer checks for interrupts after execution of every instruction.
  A. TRUE
  B. FALSE
  Explanation: If an interrupt is pending, the processor automatically jumps to the corresponding interrupt handler code, which is located in the operating system kernel and will execute in kernel mode.

## Slide 67: Sample list of interrupts
interrupt vector table (IVT)
Notes: INT is an assembly language instruction for x86 processors that generates a software interrupt. It takes the interrupt number formatted as a byte value.

## Slide 68
1
2
3
4
5
Behind the Interrupt
program status word (PSW)
Notes: An interrupt triggers a number of events, both in the processor hardware and in software. Figure 1.10 shows a typical sequence. When an I/O device completes an I/O operation, the following sequence of hardware events occurs:
The device issues an interrupt signal to the processor.
2. The processor finishes execution of the current instruction before responding to the interrupt, as indicated in Figure 1.7 .
3. The processor tests for a pending interrupt request, determines that there is one, and sends an acknowledgment signal to the device that issued the interrupt. The acknowledgment allows the device to remove its interrupt signal.
4. The processor next needs to prepare to transfer control to the interrupt routine. To begin, it saves information needed to resume the current program at the point of interrupt. The minimum information required is the program status word (PSW) and the location of the next instruction to be executed, which is contained in the program counter (PC). These can be pushed onto a control stack (see Appendix 1B).
5. The processor then loads the program counter with the entry location of the interrupt-handling routine that will respond to this interrupt. Depending on the computer architecture and OS design, there may be a single program, one for each type of interrupt, or one for each device and each type of interrupt. If there is more than one interrupt-handling routine, the processor must determine which one to invoke. This information may have been included in the original interrupt signal, or the processor may have to issue a request to the device that issued the interrupt to get a response that contains the needed information.

## Slide 69
1
2
3
4
5
What is this PC pointing to?
Notes: An interrupt triggers a number of events, both in the processor hardware and in software. Figure 1.10 shows a typical sequence. When an I/O device completes an I/O operation, the following sequence of hardware events occurs:
The device issues an interrupt signal to the processor.
2. The processor finishes execution of the current instruction before responding to the interrupt, as indicated in Figure 1.7 .
3. The processor tests for a pending interrupt request, determines that there is one, and sends an acknowledgment signal to the device that issued the interrupt. The acknowledgment allows the device to remove its interrupt signal.
4. The processor next needs to prepare to transfer control to the interrupt routine. To begin, it saves information needed to resume the current program at the point of interrupt. The minimum information required is the program status word (PSW) and the location of the next instruction to be executed, which is contained in the program counter (PC). These can be pushed onto a control stack (see Appendix 1B).
5. The processor then loads the program counter with the entry location of the interrupt-handling routine that will respond to this interrupt. Depending on the computer architecture and OS design, there may be a single program, one for each type of interrupt, or one for each device and each type of interrupt. If there is more than one interrupt-handling routine, the processor must determine which one to invoke. This information may have been included in the original interrupt signal, or the processor may have to issue a request to the device that issued the interrupt to get a response that contains the needed information.

## Slide 70
(1)
(2)
(3)
Notes: Once the program counter has been loaded, the processor proceeds to the next instruction cycle, which begins with an instruction fetch. Because the instruction fetch is determined by the contents of the program counter, control is transferred to the interrupt-handler program. The execution of this program results in the following operations:
6. At this point, the program counter and PSW relating to the interrupted program have been saved on the control stack. However, there is other information that is considered part of the state of the executing program. In particular, the contents of the processor registers need to be saved, because these registers may be used by the interrupt handler. So all of these values, plus any other state information, need to be saved. Typically, the interrupt handler will begin by saving the contents of all registers on the stack. Other state information that must be saved is discussed in Chapter 3 . Figure 1.11a shows a simple example. In this case, a user program is interrupted after the instruction at location N. The contents of all of the registers plus the address of the next instruction (N +1) , a total of M words, are pushed onto the control stack. The stack pointer is updated to point to the new top of stack, and the program counter is updated to point to the beginning of the interrupt service routine.
7. The interrupt handler may now proceed to process the interrupt. This includes an examination of status information relating to the I/O operation or other event that caused an interrupt. It may also involve sending additional commands or acknowledgments to the I/O device.
8. When interrupt processing is complete, the saved register values are retrieved from the stack and restored to the registers (e.g., see Figure 1.11b ).
9. The final act is to restore the PSW and program counter values from the stack. As a result, the next instruction to be executed will be from the previously
interrupted program.
It is important to save all of the state information about the interrupted program for later resumption. This is because the interrupt is not a routine called from the program. Rather, the interrupt can occur at any time and therefore at any point in the execution of a user program. Its occurrence is unpredictable..

## Slide 71: Multiple Interrupts
An interrupt occurs while another interrupt is being processed
e.g. receiving data from a communications line and printing results at the same time
Two approaches:
Disable interrupts while an interrupt is being processed
Use a priority scheme
Notes: So far, we have discussed the occurrence of a single interrupt. Suppose, however, that one or more interrupts can occur while an interrupt is being processed. For example, a program may be receiving data from a communications line and printing results at the same time. The printer will generate an interrupt every time that it completes a print operation. The communication line controller will generate an interrupt every time a unit of data arrives. The unit could either be a single character or a block, depending on the nature of the communications discipline. In any case, it is possible for a communications interrupt to occur while a printer interrupt is being processed.

## Slide 72
Notes: Two approaches can be taken to dealing with multiple interrupts. The first is to disable interrupts while an interrupt is being processed. A disabled interrupt simply means that the processor ignores any new interrupt request signal. If an interrupt occurs during this time, it generally remains pending and will be checked by the processor after the processor has reenabled interrupts. Thus, if an interrupt occurs when a user program is executing, then interrupts are disabled immediately. After the interrupt-handler routine completes, interrupts are reenabled before resuming the user program, and the processor checks to see if additional interrupts have occurred. This approach is simple, as interrupts are handled in strict sequential
order ( Figure 1.12a ).
The drawback to the preceding approach is that it does not take into account relative priority or time-critical needs. For example, when input arrives from the communications line, it may need to be absorbed rapidly to make room for more input. If the first batch of input has not been processed before the second batch arrives, data may be lost because the buffer on the I/O device may fill and overflow.
A second approach is to define priorities for interrupts and to allow an interrupt of higher priority to cause a lower–priority interrupt handler to be interrupted ( Figure 1.12b ).

## Slide 73
[t=20]
[t=15]
[t=10]
 | Priority
Disk | 4
Printer | 2
Communication Line | 5
Notes: As an example of this second approach, consider a system with three I/O devices: a printer, a disk, and a communications line, with increasing priorities of 2, 4, and 5, respectively. Figure 1.13 , based on an example in [TANE06], illustrates a possible sequence. A user program begins at t =0 . At t =10 , a printer interrupt occurs; user information is placed on the control stack and execution continues at the printer interrupt service routine (ISR). While this routine is still executing, at t =15 a communications interrupt occurs. Because the communications line has higher priority than the printer, the interrupt request is honored. The printer ISR is interrupted, its state is pushed onto the stack, and execution continues at the communications ISR. While this routine is executing, a disk interrupt occurs (t 20) . Because this interrupt is of lower priority, it is simply held, and the communications ISR runs to completion.
When the communications ISR is complete (t = 25) , the previous processor state is restored, which is the execution of the printer ISR. However, before even a single instruction in that routine can be executed, the processor honors the higherpriority disk interrupt and transfers control to the disk ISR. Only when that routine is complete (t = 35) is the printer ISR resumed. When that routine completes (t = 40) , control finally returns to the user program.

## Slide 74
[t=20]
[t=15]
[t=10]
 | Priority
Disk | 4
Printer | 2
Communication Line | 5
How many CPU clocks does it take for Printer, Disk and Communication Interrupt Service Routine, respectively?
Notes: As an example of this second approach, consider a system with three I/O devices: a printer, a disk, and a communications line, with increasing priorities of 2, 4, and 5, respectively. Figure 1.13 , based on an example in [TANE06], illustrates a possible sequence. A user program begins at t =0 . At t =10 , a printer interrupt occurs; user information is placed on the control stack and execution continues at the printer interrupt service routine (ISR). While this routine is still executing, at t =15 a communications interrupt occurs. Because the communications line has higher priority than the printer, the interrupt request is honored. The printer ISR is interrupted, its state is pushed onto the stack, and execution continues at the communications ISR. While this routine is executing, a disk interrupt occurs (t 20) . Because this interrupt is of lower priority, it is simply held, and the communications ISR runs to completion.
When the communications ISR is complete (t = 25) , the previous processor state is restored, which is the execution of the printer ISR. However, before even a single instruction in that routine can be executed, the processor honors the higherpriority disk interrupt and transfers control to the disk ISR. Only when that routine is complete (t = 35) is the printer ISR resumed. When that routine completes (t = 40) , control finally returns to the user program.
10 for each.

## Slide 75: Memory Hierarchy
Design constraints on a computer’s memory
    How much?
    How fast?
    How expensive?
If the capacity is there, applications will likely be developed to use it
Memory must be able to keep up with the processor
Cost of memory must be reasonable in relationship to the other components
Faster access time = greater cost per bit
Greater capacity = smaller cost per bit
Greater capacity = slower access speed
Notes: The design constraints on a computer’s memory can be summed up by three questions: How much? How fast? How expensive?
The question of how much is somewhat open ended. If the capacity is there, applications will likely be developed to use it. The question of how fast is, in a sense, easier to answer. To achieve greatest performance, the memory must be able to keep up with the processor. That is, as the processor is executing instructions, we would not want it to have to pause waiting for instructions or operands. The final question must also be considered. For a practical system, the cost of memory must be reasonable in relationship to other components.
As might be expected, there is a trade-off among the three key characteristics of memory: namely, capacity, access time, and cost. A variety of technologies are used to implement memory systems, and across this spectrum of technologies, the following relationships hold:
• Faster access time, greater cost per bit
• Greater capacity, smaller cost per bit
• Greater capacity, slower access speed
The dilemma facing the designer is clear. The designer would like to use memory technologies that provide for large-capacity memory, both because the capacity is needed and because the cost per bit is low. However, to meet performance requirements, the designer needs to use expensive, relatively lower-capacity memories with fast access times.

## Slide 76: The Memory Hierarchy
Going down the hierarchy:
  Decreasing cost per bit
  Increasing capacity
  Increasing access time
  Decreasing frequency of access to the memory by the processor
Onboard Memory (Registers, Caches, Main memory)
  Located on-board or inside the die
  Volatile
  Accessed directly during execution data-path
Secondary Memory (Auxiliary memory)
  External
  Nonvolatile
  Used to store program and data files
Notes: The way out of this dilemma is to not rely on a single memory component or technology, but to employ a memory hierarchy . A typical hierarchy is illustrated in
Figure 1.14 . As one goes down the hierarchy, the following occur:
a. Decreasing cost per bit
b. Increasing capacity
c. Increasing access time
d. Decreasing frequency of access to the memory by the processor
Thus, smaller, more expensive, faster memories are supplemented by larger, cheaper, slower memories. The key to the success of this organization is the decreasing
frequency of access at lower levels. We will examine this concept in greater detail later in this chapter, when we discuss the cache, and when we discuss virtual
memory later in this book. A brief explanation is provided at this point.
Suppose that the processor has access to two levels of memory. Level 1 contains 1,000 bytes and has an access time of 0.1 μs; level 2 contains 100,000 bytes and has an access time of 1 μs. Assume that if a byte to be accessed is in level 1, then the processor accesses it directly. If it is in level 2, then the byte is first transferred to level 1 and then accessed by the processor. For simplicity, we ignore the time required for the processor to determine whether the byte is in level 1 or level 2.

## Slide 77
Secondary Memory
Also referred to as auxiliary memory
External
Nonvolatile
Used to store program and data files
Notes: The three forms of memory just described are, typically, volatile and employ semiconductor technology. The use of three levels exploits the fact that semiconductor memory comes in a variety of types, which differ in speed and cost. Data are stored more permanently on external mass storage devices, of which the most common are hard disk and removable media, such as removable disk, tape, and optical storage. External, nonvolatile memory is also referred to as secondary memory or auxiliary memory . These are used to store program and data files, and are usually visible to the programmer only in terms of files and records, as opposed to individual bytes or words. A hard disk is also used to provide an extension to main memory known as virtual memory, which is discussed in Chapter 8 .

## Slide 78: Cache Memory
Invisible to the OS
Interacts with other memory management hardware
Processor must access memory at least once per instruction cycle
Processor execution is limited by memory cycle time
Exploit the principle of locality with a small, fast memory
Notes: Although cache memory is invisible to the OS, it interacts with other memory management hardware. Furthermore, many of the principles used in virtual memory schemes (discussed in Chapter 8 ) are also applied in cache memory.
On all instruction cycles, the processor accesses memory at least once, to fetch the instruction, and often one or more additional times, to fetch operands and/ or store results. The rate at which the processor can execute instructions is clearly limited by the memory cycle time (the time it takes to read one word from or write one word to memory). This limitation has been a significant problem because of the persistent mismatch between processor and main memory speeds: Over the years, processor speed has consistently increased more rapidly than memory access speed. We are faced with a trade-off among speed, cost, and size. Ideally, main memory should be built with the same technology as that of the processor registers, giving memory cycle times comparable to processor cycle times. This has always been too expensive a strategy. The solution is to exploit the principle of locality by providing a small, fast memory between the processor and main memory, namely the cache.

## Slide 79
Intel i7-6700 (Skylake), 4.0 GHz
L1 Cache Latency = 4-5 cycles
L2 Cache Latency = 12 cycles
L3 Cache Latency = 42 cycles
RAM Latency = 42 cycles + 51 ns
Notes: Cache memory is intended to provide memory access time approaching that of the fastest memories available and at the same time support a large memory size that has the price of less expensive types of semiconductor memories. The concept is illustrated in Figure 1.16a . There is a relatively large and slow main memory together with a smaller, faster cache memory. The cache contains a copy of a portion of main memory. When the processor attempts to read a byte or word of memory, a check is made to determine if the byte or word is in the cache. If so, the byte or word is delivered to the processor. If not, a block of main memory, consisting of some fixed number of bytes, is read into the cache and then the byte or word is delivered to
the processor. Because of the phenomenon of locality of reference, when a block of data is fetched into the cache to satisfy a single memory reference, it is likely that many of the near-future memory references will be to other bytes in the block.
Figure 1.16b depicts the use of multiple levels of cache. The L2 cache is slower and typically larger than the L1 cache, and the L3 cache is slower and typically larger than the L2 cache.

## Slide 80
Notes: Figure 1.17 depicts the structure of a cache/main memory system. Main memory consists of up to 2 n addressable words, with each word having a unique n –bit address. For mapping purposes, this memory is considered to consist of a number of fixed-length blocks of K words each. That is, there are M = 2n/K blocks. Cache consists of C slots (also referred to as lines ) of K words each, and the number of slots is considerably less than the number of main memory blocks (C<<M) . Some subset of the blocks of main memory resides in the slots of the cache. If a word in a block of memory that is not in the cache is read, that block is transferred to one of the slots of the cache. Because there are more blocks than slots, an individual slot cannot be uniquely and permanently dedicated to a particular block. Therefore, each slot includes a tag that identifies which particular block is currently being stored. The tag is usually some number of higher-order bits of the address and refers to all addresses that begin with that sequence of bits.

## Slide 81: Principle of Locality
Memory references by the processor tend to cluster (e.g. Temporal and spatial locality).
Data is organized so that the percentage of accesses to each successively lower level is substantially less than that of the level above.
Can be applied across more than two levels of memory.
Notes: The basis for the validity of condition (d) is a principle known as locality of reference [DENN68]. During the course of execution of a program, memory references by the processor, for both instructions and data, tend to cluster. Programs typically contain a number of iterative loops and subroutines. Once a loop or subroutine is entered, there are repeated references to a small set of instructions. Similarly, operations on tables and arrays involve access to a clustered set of data bytes. Over a long period of time, the clusters in use change, but over a short period of time, the processor is primarily working with fixed clusters of memory references.
Accordingly, it is possible to organize data across the hierarchy such that the percentage of accesses to each successively lower level is substantially less than that of the level above. Consider the two-level example already presented. Let level 2 memory contain all program instructions and data. The current clusters can be temporarily placed in level 1. From time to time, one of the clusters in level 1 will have to be swapped back to level 2 to make room for a new cluster coming in to level 1. On average, however, most references will be to instructions and data contained in level 1.
This principle can be applied across more than two levels of memory. The fastest, smallest, and most expensive type of memory consists of the registers internal to the processor. Typically, a processor will contain a few dozen such registers, although some processors contain hundreds of registers. Skipping down two levels, main memory is the principal internal memory system of the computer. Each location in main memory has a unique address, and most machine instructions refer to one or more main memory addresses. Main memory is usually extended with a higher-speed, smaller cache. The cache is not usually visible to the programmer or, indeed, to the processor. It is a device for staging the movement of data between main memory and processor registers to improve performance.

## Slide 82: The principle of locality
It’s usually difficult or impossible to figure out what data will be “most frequently accessed” before a program actually runs, which makes it hard to know what to store into the small, precious cache memory.
But in practice, most programs exhibit locality, which the cache can take advantage of.
  The principle of temporal locality says that if a program accesses one memory address, there is a good chance that it will access the same address again.
  The principle of spatial locality says that if a program accesses one memory address, there is a good chance that it will also access other nearby addresses.

## Slide 83: Temporal locality in data

## Slide 84: Spatial locality in data

## Slide 85
Problem Time

## Slide 86
Notes: Figure 1.18 illustrates the read operation. The processor generates the address, RA, of a word to be read. If the word is contained in the cache, it is delivered to the processor. Otherwise, the block containing that word is loaded into the cache and the word is delivered to the processor.

## Slide 87: Cache Design
Main categories are:
Cache size
Block size
Mapping function
Write policy
Number of cache levels
Replacement algorithm
Notes: A detailed discussion of cache design is beyond the scope of this book. Key elements are briefly summarized here. We will see that similar design issues must be addressed in dealing with virtual memory and disk cache design. They fall into the following categories:
• Cache size
• Block size
• Mapping function
• Replacement algorithm
• Write policy
• Number of cache levels

## Slide 88: Cache and Block Size
Cache Size
Small caches have significant impact on performance
Block Size
The unit of data exchanged between cache and main memory
Notes: We have already dealt with the issue of cache size . It turns out that reasonably small caches can have a significant impact on performance. Another size issue is that of block size : the unit of data exchanged between cache and main memory. As the block size increases from very small to larger sizes, the hit ratio will at first increase because of the principle of locality: the high probability that data in the vicinity of a referenced word are likely to be referenced in the near future. As the block size increases, more useful data are brought into the cache. The hit ratio will begin to decrease, however, as the block becomes even bigger and the probability of using the newly fetched data becomes less than the probability of reusing the data that have to be moved out of the cache to make room for the new block.

## Slide 89: Mapping Function
Two constraints affect design:
When one block is read in, another may have to be replaced
The more flexible the mapping function, the more complex is the circuitry required to search the cache
Determines which cache location the block will occupy
Notes: When a new block of data is read into the cache, the mapping function determines which cache location the block will occupy. Two constraints affect the design of the mapping function. First, when one block is read in, another may have to be replaced. We would like to do this in such a way as to minimize the probability that we will replace a block that will be needed in the near future. The more flexible the mapping function, the more scope we have to design a replacement algorithm to maximize the hit ratio. Second, the more flexible the mapping function, the more complex is the circuitry required to search the cache to determine if a given block is in the cache.

## Slide 90: Replacement Algorithm
Chooses which block to replace when a new block is to be loaded into the cache.
  Least Recently Used (LRU) Algorithm
  Effective strategy is to replace a block that has been in the cache the longest with no references to it
  Hardware mechanisms are needed to identify the least recently used block
Notes: The replacement algorithm chooses, within the constraints of the mapping function, which block to replace when a new block is to be loaded into the cache and the cache already has all slots filled with other blocks. We would like to replace the block that is least likely to be needed again in the near future. Although it is impossible to identify such a block, a reasonably effective strategy is to replace the block that has been in the cache longest with no reference to it. This policy is referred to as the least-recently-used (LRU) algorithm. Hardware mechanisms are needed to identify the least-recently-used block.

## Slide 91: Effective Access Time (EAT)
In a two-level memory system (e.g. cache and main memory):
Example: Suppose 95% of the memory accesses are found in the cache (H = 0.95) Then, assuming T1= 0.1μs and T2= 1μs, the average time to access a byte can be expressed as:
(0.95) (0.1 μs) + (0.05) (0.1 μs + 1 μs) = 0.095 + 0.055 = 0.15 μs

## Slide 92: Problem Time
Consider a memory system with the following parameters:
          Tc = 50 ns Cc = 0.003 cents/bit
          Tm = 1500 ns Cm = 0.00001 cents/bit
a) What is the cost of 1 Mbyte of main memory?
b) What is the cost of 1 Mbyte of main memory using cache memory technology?
c) If the effective access time is 10% greater than the cache access time, what is the hit ratio H?

## Slide 93: I/O Techniques
Three techniques are possible for I/O operations:
Programmed I/O
Interrupt-Driven I/O
Direct Memory Access (DMA)
When the processor encounters an instruction relating to I/O, it executes that instruction by issuing a command to the appropriate I/O module.
Notes: When the processor is executing a program and encounters an instruction relating to I/O, it executes that instruction by issuing a command to the appropriate I/O module.
Three techniques are possible for I/O operations: programmed I/O, interrupt-driven I/O, and direct memory access (DMA).

## Slide 94: Programmed I/O
The I/O module performs the requested action then sets the appropriate bits in the I/O status register
The processor periodically checks the status of the I/O module until it determines the instruction is complete
With programmed I/O the performance level of the entire system is severely degraded
busy-waiting or polling
Notes: In the case of programmed I/O , the I/O module performs the requested action and then sets the appropriate bits in the I/O status register but takes no further action to alert the processor. In particular, it does not interrupt the processor. Thus, after the I/O instruction is invoked, the processor must take some active role in determining when the I/O instruction is completed. For this purpose, the processor periodically checks the status of the I/O module until it finds that the operation is complete.
With programmed I/O, the processor has to wait a long time for the I/O module of concern to be ready for either reception or transmission of more data. The processor, while waiting, must repeatedly interrogate the status of the I/O module. As a result, the performance level of the entire system is severely degraded.

## Slide 95: Interrupt-Driven I/O
Processor issues an I/O command to a module and then goes on to do some other useful work
The processor executes the data transfer and then resumes its former processing
The I/O module will then interrupt the processor to request service when it is ready to exchange data with the processor
More efficient than Programmed I/O but still requires active intervention of the processor to transfer data between memory and an I/O module
CPU thread copies data
Notes: An alternative, known as interrupt-driven I/O , is for the processor to issue an I/O command to a module and then go on to do some other useful work. The I/O module will then interrupt the processor to request service when it is ready to exchange data with the processor. The processor then executes the data transfer, as before, and then resumes its former processing.

## Slide 96: Interrupt-Driven I/O

## Slide 97: Interrupt-Driven I/O Drawbacks
Transfer rate is limited by the speed with which the processor can test and service a device
The processor is tied up in managing an I/O transfer
      A number of instructions must be executed for each I/O transfer
Notes: Interrupt-driven I/O, though more efficient than simple programmed I/O, still requires the active intervention of the processor to transfer data between memory and an I/O module, and any data transfer must traverse a path through the processor. Thus, both of these forms of I/O suffer from two inherent drawbacks:
1. The I/O transfer rate is limited by the speed with which the processor can test and service a device.
2. The processor is tied up in managing an I/O transfer; a number of instructions must be executed for each I/O transfer.

## Slide 98: Direct Memory Access (DMA)
When the processor wishes to read or write data it issues a command to the DMA module containing:
The address of the I/O device involved
The starting location in memory to read/write
The number of words to be read/written
Whether a read or write is requested
Performed by a separate module on the system bus or incorporated into an I/O module
Notes: When large volumes of data are to be moved, a more efficient technique is required: direct memory access (DMA) . The DMA function can be performed by a separate module on the system bus or it can be incorporated into an I/O module. In either case, the technique works as follows. When the processor wishes to read or write a block of data, it issues a command to the DMA module, by sending to the DMA module the following information:
• Whether a read or write is requested
• The address of the I/O device involved
• The starting location in memory to read data from or write data to
• The number of words to be read or written

## Slide 99: Steps in a DMA transfer.

## Slide 100: Steps in a DMA transfer

## Slide 101: Steps in a DMA transfer

## Slide 102: Steps in a DMA transfer

## Slide 103: Direct Memory Access
Transfers the entire block of data directly to and from memory without going through the processor
    Processor is involved only at the beginning and end of the transfer
    Processor executes more slowly during a transfer when processor access to the bus is required
More efficient than interrupt-driven or programmed I/O
DMA HW copiesdata
Notes: The processor then continues with other work. It has delegated this I/O operation to the DMA module, and that module will take care of it. The DMA module transfers the entire block of data, one word at a time, directly to or from memory without going through the processor. When the transfer is complete, the DMA module sends an interrupt signal to the processor. Thus, the processor is involved only at the beginning and end of the transfer.
The DMA module needs to take control of the bus to transfer data to and from memory. Because of this competition for bus usage, there may be times when the processor needs the bus and must wait for the DMA module. Note that this is not an interrupt; the processor does not save a context and do something else. Rather, the processor pauses for one bus cycle (the time it takes to transfer one word across the bus). The overall effect is to cause the processor to execute more slowly during a DMA transfer when processor access to the bus is required. Nevertheless, for a multiple-word I/O transfer, DMA is far more efficient than interrupt-driven or programmed I/O.

## Slide 104: Symmetric Multiprocessors (SMP)
A stand-alone computer system with the following characteristics:
  Two or more similar processors of comparable capability
  Processors share the same main memory and are interconnected by a bus or other internal connection scheme
  Processors share access to I/O devices
  All processors can perform the same functions
  The system is controlled by an integrated operating system that provides interaction between processors and their programs at the job, task, file, and data element levels
Notes: An SMP can be defined as a stand-alone computer system with the following characteristics:
1. There are two or more similar processors of comparable capability.
2. These processors share the same main memory and I/O facilities and are interconnected by a bus or other internal connection scheme, such that memory access time is approximately the same for each processor.
3. All processors share access to I/O devices, either through the same channels or through different channels that provide paths to the same device.
4. All processors can perform the same functions (hence the term symmetric ).
5. The system is controlled by an integrated operating system that provides interaction between processors and their programs at the job, task, file, and
data element levels.
Points 1 to 4 should be self-explanatory. Point 5 illustrates one of the contrasts with a loosely coupled multiprocessing system, such as a cluster. In the latter, the physical unit of interaction is usually a message or complete file. In an SMP, individual data elements can constitute the level of interaction, and there can be a high degree of cooperation between processes.

## Slide 105: SMP Advantages
Performance
A system with multiple processors will yield greater performance if work can be done in parallel
Availability
The failure of a single processor does not halt the machine
Incremental Growth
An additional processor can be added to enhance performance
Scaling
Vendors can offer a range of products with different price and performance characteristics
Notes: An SMP organization has a number of potential advantages over a uniprocessor organization, including the following:
• Performance: If the work to be done by a computer can be organized so that some portions of the work can be done in parallel, then a system with multiple processors will yield greater performance than one with a single processor of the same type.
Availability: In a symmetric multiprocessor, because all processors can perform the same functions, the failure of a single processor does not halt the machine. Instead, the system can continue to function at reduced performance.
• Incremental growth: A user can enhance the performance of a system by adding an additional processor.
• Scaling: Vendors can offer a range of products with different price and performance characteristics based on the number of processors configured in the system.
It is important to note that these are potential, rather than guaranteed, benefits. The operating system must provide tools and functions to exploit the parallelism in an SMP system. An attractive feature of an SMP is that the existence of multiple processors is transparent to the user. The operating system takes care of scheduling of tasks on individual processors and of synchronization among processors.

## Slide 106
Notes: Figure 1.19 illustrates the general organization of an SMP.
There are multiple processors, each of which contains its own control unit, arithmetic logic unit, and registers. Each processor has access to a shared main memory and the I/O devices through some form of interconnection mechanism; a shared bus is a common facility. The processors can communicate with each other through memory (messages and status information left in shared address spaces). It may also be possible for processors to exchange signals directly. The memory is often organized so that multiple simultaneous accesses to separate blocks of memory are possible.
In modern computers, processors generally have at least one level of cache memory that is private to the processor. This use of cache introduces some new design considerations. Because each local cache contains an image of a portion of main memory, if a word is altered in one cache, it could conceivably invalidate a word in another cache. To prevent this, the other processors must be alerted that an update has taken place. This problem is known as the cache coherence problem and is typically addressed in hardware rather than by the OS.

## Slide 107
Also known as a chip multiprocessor
Combines two or more processors (cores) on a single piece of silicon (die)
    Each core consists of all of the components of an independent processor
In addition, multicore chips also include L2 cache and in some cases L3 cache
Multicore CPU
Notes: An example of a multicore system is the Intel Core i7-5960X, which includes
six x86 processors, each with a dedicated L2 cache, and with a shared L3 cache
(Figure 1.20a). One mechanism Intel uses to make its caches more effective is
prefetching, in which the hardware examines memory access patterns and attempts to
fill the caches speculatively with data that’s likely to be requested soon. Figure 1.20b
shows the physical layout of the 5960X in its chip.
The Core i7-5960X chip supports two forms of external communications to
other chips. The DDR4 memory controller brings the memory controller for the
DDR (double data rate) main memory onto the chip. The interface supports four
channels that are 8 bytes wide for a total bus width of 256 bits, for an aggregate data
rate of up to 64 GB/s. With the memory controller on the chip, the Front Side Bus is
eliminated. The PCI Express is a peripheral bus. It enables high-speed communications
among connected processor chips. The PCI Express link operates at 8 GT/s
(transfers per second). At 40 bits per transfer, that adds up to 40 GB/s.
A multicore computer, also known as a chip multiprocessor , combines two or more processors (called cores) on a single piece of silicon (called a die). Typically, each core consists of all of the components of an independent processor, such as registers, ALU, pipeline hardware, and control unit, plus L1 instruction and data caches. In addition to the multiple cores, contemporary multicore chips also include L2 cache and, in some cases, L3 cache.
The motivation for the development of multicore computers can be summed up as follows. For decades, microprocessor systems have experienced a steady, usually exponential, increase in performance. This is partly due to hardware trends, such as an increase in clock frequency and the ability to put cache memory closer to the processor because of the increasing miniaturization of microcomputer components. Performance has also been improved by the increased complexity of processor design to exploit parallelism in instruction execution and memory access. In brief, designers have come up against practical limits in the ability to achieve greater performance by means of more complex processors. Designers have found that the best way to improve performance to take advantage of advances in hardware is to put multiple processors and a substantial amount of cache memory on a single chip. A detailed discussion of the rationale for this trend is beyond our scope, but is summarized in Appendix C .

## Slide 108: Summary
Cache memory
    Motivation
    Cache principles
    Cache design
Direct memory access
Multiprocessor and multicore organization
    Symmetric multiprocessors
    Multicore CPUs
Basic Elements
Evolution of the microprocessor
Instruction execution
Interrupts
    Interrupts and the instruction cycle
    Interrupt processing
    Multiple interrupts
The memory hierarchy
Notes: Summary of Chapter 1.

## Slide 109: Question Time?

## Slide 110: Solutions